# GENERAL

## RELATED SECTIONS

### Section 01 33 00 - Submittal Procedures.

### Section 31 22 13 - Rough Grading.

### Section 32 91 19.13 - Topsoil Placement and Grading.

## SUBMITTALS

### Provide product data for:

#### Seed

#### Mulch

#### Tackifier

#### Fertilizer

### Submit in writing to Owner seven (7) working days prior to commencing work:

#### Volume capacity of hydraulic seeder in litres.

#### Amount of material to be used per tank based on volume.

#### Number of tank loads required per hectare to apply specified slurry mixture per hectare.

## QUALITY ASSURANCE

### Test Reports: certified test reports showing compliance with specified performance characteristics and physical properties.

### Certificates: product certificates signed by manufacturer certifying materials comply with specified performance characteristics and criteria and physical requirements.

### Pre-Installation Meetings: conduct pre-installation meeting to verify project requirements, installation instructions and warranty requirements.

### Contractor Qualifications:

#### Landscape Contractor: to be a Member in Good Standing of Landscape Newfoundland Green for Life (LNL).

#### Landscape Planting Supervisor: Landscape Horticulturist Journeyperson or Landscape Industry Certified Technician with Softscape Installation designation or equivalent.

#### Landscape Maintenance Supervisor: Landscape Horticulturist Journeyperson or Landscape Industry Certified Technician with Turf Maintenance designation or equivalent.

#### Provide proof of qualifications when requested by Owner.

## SCHEDULING

### Schedule hydraulic seeding to coincide with preparation of soil surface.

## WARRANTY

### All areas hydroseeded under this contract shall have a warranty period of one (1) year from the date of Certificate of Substantial Performance shall cover any defects in materials and workmanship or damages caused by the elements of weather. All defects shall be repaired to the satisfaction of the Owner at no cost to the Owner.

## DELIVERY, STORAGE and HANDLING

### Deliver, store and handle materials in accordance with Section with manufacturer's written instructions.

### Labelled bags of fertilizer identifying mass in kg, mix components and percentages, date of bagging, supplier's name and lot number.

### Inoculant containers to be tagged with expiry date.

### Store fertilizer indoors, in dry location and in accordance with manufacturer's recommendations in clean, dry, well-ventilated area.

### Replace defective or damaged materials with new.

# PRODUCTS

## MATERIALS

### Seed: "Canada pedigreed grade" in accordance with Government of Canada Seeds Act and Regulations.

#### Grass mixture: "Certified", "Canada No. 1 Lawn Grass Mixture" in accordance with Government of Canada "Seeds Act" and "Seeds Regulations".

##### Contractor to submit mixture composition to Owner for approval.

### Mulch: specially manufactured for use in hydraulic seeding equipment, non-toxic, water activated, green colouring, free of germination and growth inhibiting factors with following properties:

#### Type I mulch:

##### Made from wood cellulose fibre.

##### Organic matter content: 95% plus or minus 0.5%.

##### Value of pH: 6.0.

##### Potential water absorption: 800-900%.

#### Type II mulch:

##### Made from newsprint, raw cotton fibre and straw, processed to produce fibre lengths of 15 mm minimum and 25 mm maximum. Greater proportions of ingredients to be straw.

### Tackifier: water dilutable, liquid dispersion.

### Water: free of impurities that would inhibit germination and growth.

### Fertilizer:

#### To Canada "Fertilizers Act" and "Fertilizers Regulations".

#### Complete synthetic, slow release with 35% of nitrogen content in water-insoluble form.

# EXECUTION

## WORKMANSHIP

### Do not spray onto structures, signs, guide rails, fences, plant material, utilities and other than surfaces intended.

### Clean-up immediately, any material sprayed where not intended, to satisfaction of Owner.

### Do not perform work under adverse field conditions such as wind speeds over 10 km/h, frozen ground or ground covered with snow, ice or standing water.

### Protect seeded areas from trespass until plants are established.

## PREPARATION OF SURFACES

### Do not perform work under adverse field conditions such as wind speeds over 10 km/h, frozen ground or ground covered with snow, ice or standing water.

### Fine grade areas to be seeded free of humps and hollows. Ensure areas are free of deleterious and refuse materials.

### Cultivated areas identified as requiring cultivation to depth of 25 mm.

### Ensure areas to be seeded are moist to depth of 150 mm before seeding.

### Obtain Owner approval of grade and topsoil depth before starting to seed.

## FERTILIZING PROGRAM

### Fertilize prior to fine grading incorporating fertilizer equally distributed in accordance with an agreed program between Contractor and Owner.

### Fertilize during establishment and warranty periods to an agreed program between Contractor and Owner.

## PREPARATION OF SLURRY

### Measure quantities of materials by weight or weight-calibrated volume measurement satisfactory to Owner.  Supply equipment required for this work.

### Charge required water into seeder. Add material into hydraulic seeder under agitation. Pulverize mulch and charge slowly into seeder.

### After all materials are in the seeder and well mixed, charge tackifier into seeder and mix thoroughly to complete slurry.

## SLURRY APPLICATION

### Hydraulic seeding equipment:

#### Slurry tank.

#### Agitation system for slurry to be capable of operating during charging of tank and during seeding, consisting of recirculation of slurry and or mechanical agitation method.

#### Pumps capable of maintaining continuous non-fluctuating flow of solution.

#### Supplied with not less than 6 spray pattern nozzles.

#### Capable of seeding by 50 m hand operated hoses and appropriate nozzles.

#### Tank volume to be certified by certifying authority and identified by authorities "Volume Certification Plate".

### Slurry mixture applied per hectare.

#### Seed: Grass mixture 150 kg.

#### Mulch: Type I 1250 kg.

#### Tackifier: 20 kg.

#### Water: Minimum 30,000 L.

#### Fertilizer: 600 kg, ratio 5-20-20.

### Apply slurry uniformly, at optimum angle of application for adherence to surfaces and germination of seed.

#### Using correct nozzle for application.

#### Using hoses for surfaces difficult to reach and to control application.

### Blend application 300 mm into adjacent grass areas or sodded areas to form uniform surfaces.

### Re-apply where application is not uniform.

### Remove slurry from items and areas not designated to be sprayed.

### Protect seeded areas from trespass satisfactory to Owner.

### Remove protection devices as directed by Owner.

## MAINTENANCE DURING ESTABLISHMENT PERIOD

### Perform following operations from time of seed application until acceptance by Owner.

### Grass Mixture:

#### Repair and reseed dead or bare spots to allow establishment of seed prior to acceptance.

#### Mow grass to 50 mm whenever it reaches height of 70 mm. Remove clippings which will smother grass as directed by Owner.

#### Fertilize seeded areas ten (10) weeks after germination provided plants have mature true leafs in accordance with fertilizing program. Spread half of required amount of fertilizer in one direction and remainder at right angles; water in well.

#### Control weeds by manual, mechanical or chemical means. Utilizing acceptable integrated pest management practices.

#### Water seeded area to maintain optimum soil moisture level for germination and continued growth of grass. Control watering to prevent washouts.

## ACCEPTANCE

### Seeded areas will be accepted by Owner provided that:

#### Plants are uniformly established. Seeded areas are free of rutted, eroded, bare or dead spots.

#### Areas have been mown at least twice.

#### Areas have been fertilized.

### Areas seeded in fall will achieve final acceptance in following spring, one month after start of growing season provided acceptance conditions are fulfilled.

## MAINTENANCE DURING WARRANTY PERIOD

### Perform following operations until acceptance of Certificate of Total Performance.

#### Water seeded area to maintain optimum soil moisture level for continued growth. Control watering to prevent washouts.

#### Repair and reseed dead or bare spots to satisfaction of Owner.

#### Mow areas seeded, remove clippings, as directed by Owner.

#### Fertilize seeded areas in accordance with fertilizing program. Spread half of required amount of fertilizer in one direction and remainder at right angles and water in well.

#### Eliminate weeds by mechanical or chemical means.

#### At the end of the warranty period repeat items 2-5.

## CLEANING

### Upon completion of installation, remove surplus materials, rubbish, tools and equipment barriers.

END OF SECTION