# General

## RELATED SECTIONS

### Section 01 33 00 - Submittal Procedures.

### Section 01 74 21 - Construction / Demolition Waste Management and Disposal.

### Section 01 78 00 - Closeout Submittals.

### Section 21 05 01 - Common Work Results for Mechanical.

### Section 22 11 18 - Domestic Water Piping Copper.

### Section 23 05 23.02 - Valves Cast Iron.

### Section 33 11 16 - Site Water Utility Distribution Piping.

## REFERENCES

### American National Standards Institute/American Water Works Association (ANSI/AWWA)

#### ANSI/AWWA C104/A21.4, Cement-Mortar Lining for Ductile-Iron Pipe and Fittings for Water.

#### ANSI/AWWA C110/A21.10, Ductile Iron and Gray Iron Fittings, 3 inch through 48 inch for Water and Other Liquids.

#### ANSI/AWWA C111/A21.11, Rubber Gasket Joints for Ductile-Iron and Gray-Iron Pressure Pipe and Fittings.

#### ANSI/AWWA C151/A21.51, Ductile-Iron Pipe, Centrifugally Cast, for Water.

### American Society for Testing and Materials International, (ASTM)

#### ASTM A307, Specification for Carbon Steel Bolts and Studs, 60,000 psi Tensile Strength.

### Manufacturer's Standardization Society of the Valve and Fittings Industry

#### MSS-SP-70, Cast Iron Gate Valves, Flanged and Threaded Ends.

## PRODUCT DATA

### Submit product data in accordance with Section 01 33 00 - Submittal Procedures.

### Submit data for following: valves, couplings, mechanical joints.

## CLOSEOUT SUBMITTALS

### Provide maintenance data for incorporation into manual specified in Section   01 78 00 - Closeout Submittals.

## WASTE MANAGEMENT AND DISPOSAL

### Separate and recycle waste materials in accordance with Section 01 74 21 – Construction /Demolition Waste Management and Disposal.

### Remove from site and dispose of packaging materials at appropriate recycling facilities.

### Collect and separate for disposal paper, plastic, polystyrene, corrugated cardboard, packaging material in appropriate on-site bins for recycling in accordance with Waste Management Plan.

### Divert unused metal and wiring materials from landfill to metal recycling facility approved by Owner.

# Products

## PIPE

### Service water pipe: ductile iron cement mortar lined from 1 m outside of building or as indicated to:

#### Ductile iron: ANSI/AWWA C151/A21.51.

#### Cement mortar lining for ductile iron pipe: to ANSI/AWWA C104/A21.4.

## FITTINGS

### NPS 3 and larger mechanical joints or flanged: to ANSI/AWWA C110/A21.10.

## JOINTS

### Rubber gaskets for mechanical joints or flanges: to ANSI/AWWA C111/A21.11.

### Bolts, nuts, hex head with washers: to ASTM A307, heavy series.

## GATE VALVES

### Rising stem: to MSS SP-70, class 125, 860 kPa, flat flange faces, cast-iron body, bronze trim, bolted bonnet.

# Execution

## INSTALLATION

### Install in accordance with Canadian Plumbing Code and local authority having jurisdiction.

### Piping cut square, reamed, free of cuttings and foreign material.

### Minimum depth of bury: 1500 mm.

### Lay buried piping in compacted washed sand in accordance with AWWA Class "B" bedding. Where existing ground below bedding is unstable, install pipe on continuous concrete support.

### Where piping enters building, provide support, and seal with modular link type seal with sleeve against ingress of moisture; to approval of authority having jurisdiction.

### Assemble piping using fittings manufactured to ANSI standards and in accordance with manufacturer's instructions.

### Apply one layer of protective coating to buried piping.

## PRESSURE TESTING

### Conform to Section 21 05 01 – Common Work Results for Mechanical.

### Submit reports for inclusion into Commissioning Manuals.

## DISINFECTION

### Coordinate with Section 33 11 16 – Site Water Utility Distribution Piping and Section 22 11 18- Domestic Water Piping Copper.

### Submit bacteriological reports for inclusion into Commissioning Manuals.

END OF SECTION