# GENERAL

## SECTION INCLUDES

### Materials and installation for foundation and underslab drainage.

## RELATED SECTIONS

### Section 03 10 00 – Concrete Forms and Accessories.

### Section 31 05 16 – Aggregates for Earthwork.

### Section 31 23 33.01 - Excavating, Trenching and Backfilling.

## REFERENCES

### Canadian General Standards (CSA International).

#### CSA –A23.1/A23.,Concrete Materials and Methods of Concrete Construction/Methods of Test for Concrete.

#### CSA B1800, Plastic Non-pressure Pipe Compendium - B1800 Series (Consists of B181.1, B181.2, B181.3, B181.5, B182.1, B182.2, B182.4, B182.6, B182.7, B182.8 and B182.11).

##### CSA B182.2-02, PVC Sewer Pipe and Fittings (PSM Type).

### American Society for Testing and Materials International, (ASTM).

#### ASTM D698, Standard Test Method for Laboratory Compaction Characteristics of Soil Using Standard Effort (12,400 ft-lbf/ft3 (600 kN-m/m³)

## SITE CONDITIONS

### Examine sub-surface investigation report.

### Known underground utility lines and buried objects are as indicated on site plans.

## SUbmittals

### Submit manufacturer’s test data and certification at least two (2) weeks prior to commencing work.

#### Certification to be marked on pipe.

### Submit manufacturer’s information data sheets and instructions.

## DELIVERY, STORAGE AND HANDLING

### Deliver, store and handle materials in accordance with Section 01 61 00 – Common Product Requirements.

# PRODUCTS

## BEDDING AND SURROUND MATERIALS

### Coarse filter aggregate: to CSA-A23.1/A23.2, Group 1 20-5 mm.

### Fine filter aggregate: to CSA-A23.1/A23.2.

### Rigid plastic pipe and fittings: to CSA-B182.1, perforated size 150 mm, complete with fittings.

## BACKFILL MATERIAL

### Type 2, in accordance with Section 31 23 33.01 - Excavating, Trenching and Backfilling.

### Excavated or graded material existing on site may be suitable to use if approved by Owner.

# EXECUTION

## EXAMINATION

### Ensure graded base conforms with required drainage pattern before placing bedding material.

### Ensure improper slopes, unstable areas, areas requiring additional compaction or other unsatisfactory conditions are corrected to approval of Owner.

### Ensure foundation wall and dampproofing have been installed and approved by Owner before placing bedding material.

## BEDDING PREPARATION

### Cut trenches in base and place bedding material in uniform layers not exceeding 150 mm compacted thickness to depth as indicated.

### Shape bed true to grade and to provide continuous, uniform bearing surface for pipe.

### Shape transverse depressions, as required, to suit joints.

### Compact each layer full width of bed to at least 95% of corrected maximum dry density.

### Fill excavation below design elevation of bottom of specified bedding with compacted bedding material or lean mix concrete.

## PIPE OR TUBING INSTALLATION

### Ensure pipe interior and coupling surfaces are clean before laying.

### Lay perforated pipe tubing level minimum to slope of 1:100. Face perforations and coupling slots downward.

### Lay non-perforated pipe to slope of 1:50 from perforated pipe to disposal area. Make joints watertight.

### Grade bedding to establish pipe slope.

### Install end plugs at ends of collector drains to protect pipe tubing ends from damage and ingress of foreign material.

### Connect non-perforated pipe storm sewer by appropriate adapters manufactured for this purpose.

### Provide cleanouts on non-perforated pipe at changes of pipe direction and in runs greater than 15 m.

### Provide flush cleanouts where directed by Owner.

### Connect drainage system to building storm sewers, as indicated.

### Provide certificate of quality compliance upon satisfactory completion of installation.

## PIPE OR TUBING SURROUND MATERIAL

### Upon completion of pipe tubing laying and after Owner has inspected Work in place, surround and cover pipe as indicated.

### Hand place surround material in uniform layers not exceeding 150 mm compacted thickness, as indicated.

### Place layers uniformly and simultaneously on each side of pipe.

### Compact each layer from pipe invert to mid-height of pipe to at least 95% of corrected maximum dry density.

### Compact each layer from mid-height of pipe to underside of backfill to at least 90% of corrected maximum dry density.

## BACKFILL MATERIAL

### Place backfill material above pipe surround in uniform layers not exceeding 150 mm compacted thickness up to grades as indicated.

### Under paving and walks, compact backfill to at least 95% corrected maximum dry density. In other areas, compact to at least 90% corrected maximum dry density.

END OF SECTION