# General

## Section Includes

### Provision of rigid conduit and concrete - encased underground service ducts.

## Related Sections

### Section 01 33 00 – Submittal Procedures.

### Section 01 74 21 – Construction/Demolition Waste Management and Disposal.

### Section 26 05 00 - Common Work Results - Electrical.

### Section 26 05 27 – Grounding – Primary.

### Section 26 05 28 - Grounding - Secondary.

### Section 26 05 34 - Conduits, Conduit Fastenings and Conduit Fittings.

### Section 26 05 43.01 - Installation of Cables in Trenches and in Ducts.

### Section 26 09 23.01 - Metering and Switchboard Instruments.

### Section 26 28 13.02 – Outdoor Load Break Switches and Fuses.

### Section 33 65 73 – Concrete Encased Duct Banks and Manholes.

### Section 33 65 76 - Direct Buried Underground Cable Ducts.

### Section 33 71 20 – Electrical Pole Lines and Hardware.

## References

### Canadian Standards Association (CSA)

#### CSA A23.1/A23.2, Concrete Materials and Methods of Concrete Construction/Methods of Test for Concrete.

## Regulatory Requirements

### Co-ordinate and meet requirements of power supply authority. Ensure availability of power when required.  Use cash allowance as per Section 01 21 00 – Allowances to cover costs associated with contribution-in-aid of construction to Utility authority for provision of building permanent power supply.

# Products

## Materials

### Underground ducts: to Section 33 65 76 - Direct Buried Underground Cable Ducts, rigid PVC type, size as indicated and Section 33 65 73 – Concrete Encased Duct Banks, FRE type.

### Epoxy coated rigid steel galvanized conduit and fittings: to Section 26 05 34 - Conduits, Conduit Fastenings and Conduit Fittings. Use for sections extending above finished grade.

### Conductors: copper, type RWU-90, to Section 26 05 21 – Wires and Cables (0 -1000v), size and number of conductors as indicated.

### Meter socket: weatherproof, to Section 26 09 23.01 - Metering and Switchboard Instruments.

### Pole mounted outdoor loadbreak switch as per Section 26 28 13.02 – Outdoor Load Break Switches and Fuses.

### Concrete: to CSA A23.1/A23.2 and Division 3 - Concrete.

### Ground at terminal pole enclosure as per Section 26 05 27 - Grounding – Primary.

### Backfill: clean and free from debris.

### Pulling Iron:

#### 22 mm diameter hot dipped galvanized steel bar with exposed triangular shaped opening.

# Execution

## MANUFACTURER’S INSTRUCTIONS

### Compliance: comply with manufacturer’s written recommendations or specifications including product technical bulletins, handling, storage and installation instructions, and datasheets.

## Installation

### Install cables in trenches and in ducts in accordance with Section 26 05 43.01 - Installation of Cables in Trenches and in Ducts.

### Allow adequate conductor length for connection to supply by power supply authority.

### Install meter socket and conduit.

### Install pole mounted loadbreak switch as per Section 26 28 13.02 – Outdoor Load Break Switches and Fuses.

### Allow adequate conductor length for connection to service equipment.

### Make grounding connections in accordance with Section 26 05 28 - Grounding - Secondary.

### Provide concrete encasement in accordance with CSA A23.1 and as indicated on drawings.

### Install pulling irons as required.

### Seal ducts and conduits at building entrance location after installation of cable.

## Field Quality Control

### Perform tests in accordance with Section 26 05 00 - Common Work Results - Electrical and Section 01 91 13.13 – Commissioning (Cx) Requirements.

### Perform additional tests as required by authority having jurisdiction.

### Submit written test results for review and approval.

## CLEANING

### Proceed in accordance with Section 01 74 00 – Cleaning.

### On completion and verification of performance of installation, remove surplus materials, excess materials, rubbish, tools and equipment.

END OF SECTION